SAFETY FOR

LAWN AND GARDEN SERVICES

SAFETY AND HEALTH TRAINING

Safety and Health Orientation

Workplace safety and health orientation begins on the first day of initial employment or job transfer.  Each employee has access to a copy of this safety manual, through his or her supervisor, for review and future reference, and will be given a personal copy of the safety rules, policies, and procedures pertaining to his or her job.  Supervisors will ask questions of employees and answer employees' questions to ensure knowledge and understanding of safety rules, policies, and job-specific procedures described in our workplace safety program manual.

All employees will be instructed by their supervisors that compliance with the safety rules described in the workplace safety manual is required.

Job-Specific Training

•	Supervisors will initially train employees on how to perform assigned job tasks safely.

•	Supervisors will carefully review with each employee the specific safety rules, policies, and procedures that are applicable and that are described in the workplace safety manual.

•	Supervisors will give employees verbal instructions and specific directions on how to do the work safely.

•	Supervisors will observe employees performing the work.  If necessary, the supervisor will provide a demonstration using safe work practices, or remedial instruction to correct training deficiencies before an employee is permitted to do the work without supervision.

•	All employees will receive safe operating instructions on seldom-used or new equipment before using the equipment.

•	Supervisors will review safe work practices with employees before permitting the performance of new, non-routine, or specialized procedures.

Periodic Retraining of Employees

All employees will be retrained periodically on safety rules, policies and procedures, and when changes are made to the workplace safety manual.

Individual employees will be retrained after the occurrence of a work-related injury caused by an unsafe act or work practice, and when a supervisor observes employees displaying unsafe acts, practices, or behaviors.

FIRST AID PROCEDURES

EMERGENCY PHONE NUMBERS

Safety Coordinator	                            	Poison Control

First Aid 		                            	Fire Department

Ambulance 		                            	Police

Medical Clinic

Clinic Address

Minor First Aid Treatment

First aid kits are kept in the front office and in the service vehicles.  If you sustain an injury or are involved in an accident requiring minor first aid treatment:

•	Inform your supervisor.

•	Administer first aid treatment to the injury or wound.

•	If a first aid kit is used, indicate usage on the accident investigation report.

•	Access to a first aid kit is not intended to be a substitute for medical attention.

•	Provide details for the completion of the accident investigation report.

Non-Emergency Medical Treatment

For non-emergency work-related injuries requiring professional medical assistance, management must first authorize treatment.  If you sustain an injury requiring treatment other than first aid:

•	Inform your supervisor.

•	Proceed to the posted medical facility.  Your supervisor will assist with transportation, if necessary.

•	Provide details for the completion of the accident investigation report.

Emergency Medical Treatment

If you sustain a severe injury requiring emergency treatment:

•	Call for help and seek assistance from a co-worker.

•	Use the emergency telephone numbers and instructions posted on the first aid kit to request assistance and transportation to the local hospital emergency room.

•	Provide details for the completion of the accident investigation report.

First Aid Training

Each employee will receive training and instructions from his or her supervisor on our first aid procedures.

FIRST AID INSTRUCTIONS

In all cases requiring emergency medical treatment, immediately call, or have a co-worker call, to request

emergency medical assistance.

WOUNDS:

Minor:  Cuts, lacerations, abrasions, or punctures

•	Wash the wound using soap and water; rinse it well.

•	Cover the wound using clean dressing.

Major:  Large, deep and bleeding

•	Stop the bleeding by pressing directly on the wound, using a bandage or cloth.

•	Keep pressure on the wound until medical help arrives.

BROKEN BONES:

•	Do not move the victim unless it is absolutely necessary.

•	If the victim must be moved, "splint" the injured area.  Use a board, cardboard, or rolled newspaper as a splint.

BURNS:

Thermal (Heat)

•	Rinse the burned area, without scrubbing it, and immerse it in cold water; do not use ice water.

•	Blot dry the area and cover it using sterile gauze or a clean cloth.

Chemical

•	Flush the exposed area with cool water immediately for 15 to 20 minutes.

EYE INJURY:

Small particles

•	Do not rub your eyes.

•	Use the corner of a soft clean cloth to draw particles out, or hold the eyelids open and flush the eyes continuously with water.

Large or stuck particles

•	If a particle is stuck in the eye, do not attempt to remove it.

•	Cover both eyes with bandage.

Chemical

•	Immediately irrigate the eyes and under the eyelids, with water, for 30 minutes.

NECK AND SPINE INJURY:

•	If the victim appears to have injured his or her neck or spine, or is unable to move his or her arm or leg, do not attempt to move the victim unless it is absolutely necessary.

HEAT EXHAUSTION:

•	Loosen the victim's tight clothing.

•	Give the victim "sips" of cool water.

•	Make the victim lie down in a cooler place with the feet raised.

SAFETY RULES, POLICIES, AND PROCEDURES

The safety rules contained on these pages have been prepared for your guidance and protection in your daily work.  Employees are to study these rules carefully, review them often and observe these precautions and good common sense in carrying out their duties.

LAWN MAINTENANCE PERSONNEL

General Rules

1.	When working outdoors during the day, wear sun block, a long sleeve shirt, a hat and long pants.

2.	Stop lawn maintenance operations during an electrical storm and when lightning is visible or thunder is heard.

3.	Use work gloves when handling tree stumps and branches.

4.	Remove your gloves and wash your hands with soap and water after handling tree stumps and branches.

Lifting Procedures

1.	Plan the move before lifting; remove obstructions from your chosen pathway.

2.	Test the weight of the load before lifting by pushing the load along its resting surface.

3.	If the load is too heavy or bulky, use a wheelbarrow or get assistance from a co-worker.

4.	If assistance is required to perform a lift, coordinate and communicate your movements with those of your co-worker.

5.	Position your feet 6 to 12 inches apart with one foot slightly in front of the other.

6.	Face the load.

7.	Bend at the knees, not at the back.

8.	Keep your back straight.

9.	Get a firm grip on the object with your hands and fingers.  Use handles when present.

10.	Never lift anything if your hands are greasy or wet.

11.	Wear protective gloves when lifting branches or clippings with thorns or jagged edges.

12.	Hold objects as close to your body as possible.

13.	Perform lifting movements smoothly and gradually; do not jerk the load.

14.	If you must change direction while lifting or carrying the load, pivot your feet and turn your entire body.  Do not twist at the waist.

15.	Set down objects in the same manner as you picked them up, except in reverse.

16.	Slide materials to the end of the tailgate before attempting to lift them off of a pick-up truck.  Do not lift over the walls or tailgate of the truck bed.

Ladders and Step Ladders

1.	Read and follow the manufacturer's instructions label affixed to the ladder if you are unsure how to use the ladder.

2.	Do not use ladders that have loose rungs, cracked or split side rails, missing rubber foot pads, or other visible damage.

3.	Remove buildup of material such as dirt or mud.

4.	Allow only one person on the ladder at a time.

5.	Face the ladder when climbing up or down.

6.	Maintain a three-point contact by keeping both hands and one foot or both feet and one hand on the ladder at all times when climbing up or down.

7.	When performing work from a ladder, face the ladder and do not lean backward or sideways from the ladder.

LAWN MAINTENANCE PERSONNEL

Ladders and Step Ladders (Continued)

8.	Do not stand on the top two rungs of any ladder.

9.	Do not stand on a ladder that wobbles, or that leans to the left or right.

10.	Secure the ladder in place by having another employee hold it.

11.	Do not carry items in your hands while climbing up or down a ladder.

12.	Do not try to "walk" a ladder by rocking it.  Climb down the ladder, and then move it.

Gasoline Powered Lawn Maintenance Tools

1.	Wear safety glasses, a dust mask and closed toe shoes when operating any mower, edger, chain saw, line trimmer, or any other gasoline powered lawn maintenance tool.

2.	Do not use a chain saw, lawn mower, or any other gasoline powered lawn tool if you are taking medication from a container labeled "May cause drowsiness".

3.	Read and follow the manufacturer's routine and preventive maintenance schedule posted on the workshop wall.

4.	Do not use tools with parts that are loose, worn, cracked or otherwise visibly damaged.

5.	Tag damaged tools "Out of Service" to prevent accidental start up or use.

6.	Do not alter or by-pass any safety device provided by the manufacturer.

7.	Use only the grip locations, as specified by the manufacturer, as handholds when operating the unit.

8.	Do not pour fuel into the tank of a running engine.

9.	Do not smoke while servicing, using or refueling a gasoline powered tool.

10.	Keep body parts and clothing away from the running engine and the cutting blade.

11.	Do not run a gasoline engine inside the storage shed.

12.	Turn off the engine when you are not cutting or trimming.

13.	Allow the engine to cool before performing maintenance or refueling.

14.	Stop the engine and disconnect the spark plug wire before cleaning, inspecting, adjusting or repairing cutting blades or other rotating parts.

15.	Allow the engine to cool before covering or storing it in the storage shed.

Mowing

1.	Before entering fenced back yards, check for dogs by shaking the gate. If a dog is present, ask the owner to restrain the dog until you finish your job; check again before entering.

2.	Visually inspect the area to be mowed.  Remove or mow around hazards such as tree stumps, roots, rocks, branches, sprinklers, hoses, electrical cords, light fixtures, pipes, clothes lines and toys.

3.	Never by-pass the kill switch on the mower handle.

4.	Only the operator is permitted to ride on a riding mower.

5.	Put the mower into neutral before starting or shutting off a riding power mower.

6.	Do not place hands or feet under the mower deck.

7.	Do not direct the grass discharge towards bystanders.

8.	Empty the grass catcher to avoid clogging the mower.

LAWN MAINTENANCE PERSONNEL

Mowing (Continued)

9.	Turn off the mower before dumping the grass catcher or removing clogged grass from the chute.

10.	When using a riding mower, mow up and down the slope.  Do not mow across a slope.

11.	To mow across a slope, use an upright mower.

12.	Keep the mower in gear when going down slopes.

Edging

1.	Do not start an edger with the blade touching the ground.

2.	Do not allow anyone to stand in front of or on the unguarded side of the blade while the edger is in operation.

3.	Operate the edger at full blade speed.

4.	When edging along roads, driveways or parking lots, stay as close to the curb as possible.

Line Trimming/Weed Eaters/Brushcutters

•	Before refueling, remove the trimmer from your harness, place the trimmer on the ground and allow the engine to cool.

Backpack Blowers

1.	Do not use the blower to clean yourself.

2.	Do not direct the blower toward bystanders.

Chain Saws

1.	When transporting a chain saw by hand, stop the engine, grip the saw handle, place the muffler at the side away from your body and position the guide bar to the rear.

2.	Do not remove the chain brake or alter handles, chain brake, chain or covers.

3.	Always start a chain saw with a 10 inch or larger bar on the ground.  Engage the chain brake, place one foot through the bottom handle, hold the top handle and pull the starter rope.

4.	Do not place a chain saw on your knee when starting it.

5.	Always use both hands to maintain control of the chain saw.

6.	When moving from tree to tree or cut to cut, activate the chain brake, remove your finger from the trigger and keep the bar away from your body.

7.	Do not operate a chain saw above your shoulder height.

8.	To prevent kickback, keep the nose of the bar clear of other nearby objects during cutting.

9.	Do not set a saw down while the blade is engaged.

10.	Stop the engine and turn the switch to "OFF" when the chain saw is to be left unattended.

LAWN MAINTENANCE PERSONNEL

Hedge and Tree Trimming

1.	Wear long sleeves, long pants and gardening gloves when trimming hedges or when picking up cuttings from thorny shrubs.

2.	If you discover a bee hive or wasp nest while hedging or trimming, use the long distance aerosol insecticide labeled "Wasp and Bee Insecticide" to spray the nest.  Test with the stick or pole to ensure that all bees or wasps are gone before continuing work.

3.	Seek first aid immediately if bitten or stung by wasps or bees.

4.	Do not handle caterpillars or other insects with your bare hands.

5.	Do not wear dangling jewelry while using hedge clippers.

6.	Position yourself so that your hedge and tree cutting movements are performed below your shoulder level.

7.	Do not break branches, sticks or twigs over your legs or knees or under your feet.  Use clippers, shears or a saw to cut them.

8.	Do not perform trimming of a limb if the limb is within 10 ft. of power lines.

9.	Do not leave saws, clippers, shovels, rakes, and other equipment lying around in the work area.

Hand Saws

1.	Keep control of saws by releasing downward pressure at the end of the stroke.

2.	Do not use a saw that has dull saw blades.

3.	Oil saw blades after each use.

4.	Keep hands and fingers away from the saw blade while using the saw.

5.	Do not carry a saw by the blade.

6.	Return saws, clippers, and other cutting tools to their sheaths or guarded storage place after use.

Vehicle/Trailer Safety

1.	Set the parking brake in the towing vehicle and use wheel blocks to chock the wheels of the trailer before removing any equipment from the trailer.

2.	Secure equipment and fuel tanks to the vehicle with chains or straps to eliminate or minimize shifting of the load.

3.	No one is permitted to ride in the trailer.

4.	Use ramps to load and unload mowers and edgers from the trailer.

5.	Take slow, wide turns when towing trailers.

6.	Do not exceed the load capacity as posted on the door of the trailer.

7.	Do not place all the heavy equipment on one side of the trailer.

LAWN MAINTENANCE PERSONNEL

Lawn Mower Blade Removal and Sharpening

1.	Turn off the mower and remove the spark plug wire before removing the blade.

2.	Use an extension ratchet, or an offset wrench, to remove cutting blades.  If the equipment is fitted with a blade lockdown device, engage the lockdown before beginning the blade removal/installation process.  If no lockdown device is available, keep the blade from turning or slipping by holding it with a gloved hand.

3.	Do not use grinding wheels that have chips, cracks or grooves.

4.	Do not use the grinding wheel if it wobbles.  Tag it "Out of Service".

5.	Adjust the tongue guard so that it is no more than 1/4 inch from the grinding wheel.

6.	Do not try to stop the grinding wheel with your hand, even if you are wearing gloves.

7.	Allow blade to cool for 5 minutes after sharpening before reinstalling it on the mower.

PESTICIDE AND FERTILIZER SPRAYING OPERATORS

Pesticide and Fertilizer Spraying

1.	Do not handle or spray pesticides if you have open cuts or scratches on exposed skin surfaces on your arms or hands.

2.	Visually inspect the area to be sprayed for trip hazards, low branches, and clothes lines before beginning the job.  Avoid these hazards as you spray.

3.	Keep containers labeled "Pesticides" tightly closed when you have finished using them.

4.	Do not transfer pesticides or fertilizers into an unmarked or unlabeled container.

5.	Do not transport a pesticide container in the cab of a service vehicle.

6.	Always spray downwind; do not stand downwind when others are spraying.

7.	Do not smoke or carry smoking materials while handling or spraying from containers labeled "Pesticide" or "Fertilizer".

8.	Wash pesticide contaminated clothes separately from other clothing.

9.	Carry fresh water and soap in the service vehicle when you are going to a pesticide or fertilizer spraying job.

10.	Remove work clothes immediately whenever clothing becomes soaked or wet with liquids from containers labeled "pesticide".

11.	Walk through areas to be sprayed before spraying, and remove or "flag" low branches and clothes lines before spraying.  Stand clear of these trip hazards as you spray.

12.	Do not use empty or washed containers labeled "Pesticide" as eating or drinking containers.

13.	At the end of the workday, spray operators must remove their work clothes and take a shower in the employee locker room before going home.

14.	Refill the containers labeled "Handwash", "Soap Cleanser" and "Drinking Water" that are on the service vehicles before going to a pesticide or fertilizer spraying job.  Do not drink from the "Handwash" container; do not wash hands from the "Drinking Water" container.